## Slide 1: Interfacing with the Internet + Raspberry Pi Development Board
Alex Taylor
Capstone Project
Spring 2013
Southern Utah University

## Slide 2: Project Overview
Connecting physical devices with various internet services
  Twitter
  Facebook
  Gmail
  Etc.
Utilize Raspberry Pi plug computer
  Additionally develop a full featured development board for interfacing with the Pi

## Slide 3: Motivation
The increase of internet services that influence our daily lives
Our only connection to the internet is through a screen
To make development for the Raspberry Pi simpler and easier than what currently exists.
Notes: -The sheer number of hours spent each day looking at a computer screen.
-Lack of diversity in information consumption (other than monitors)

## Slide 4: About the Raspberry Pi
$25 single-board computer about the size of a credit card
Launched March 2012 in the UK
Developed originally for educational purposes
1 Million sold in the first year

## Slide 5: Hardware Specification
700Mhz ARM Processor
256/512MB RAM
HDMI Video Output
SD Storage
10/100 Ethernet Port
300mA/700mA power usage (1.5W/3.5W)
Weighs 45 grams
Notes: Still has the ability to play 1080p Video

## Slide 6
Notes: Powered by cell phone charger

## Slide 7: First Steps
Install and configure OS
Disable video
Connect to the internet
Notes: -Raspbian Linux
-Headless because I did not have a screen, and more ram available.
-Internet connection sharing via windows

## Slide 8: Interfacing with GPIO
26 Pin GPIO header
All GPIO pins are 3.3V, and are not 5V tolerant
Maximum current through all 3.3V pins is 50mA
Maximum Current per individual pin is 16mA
Notes: -Go over the GPIO pins seperately
-If the 5v Pin is shorted to any other pin (besides gnd) it could brick the Pi

## Slide 9: Protecting the Pi
Zener diodes
Optical Isolation
IO expander chips (SPI or I2C)
Buffer IC
  74HC244
74HC244
Notes: Protect the Pi from current and voltage
Go over the reasons I did not use them

## Slide 10: Early Tests
First test using the buffer IC and an optical isolator
Simple control of GPIO using Python
Notes: -Limitation of 74HC244 to 6mA per pin.
-Also note the 74244 Being powered by the 5V pin converting the 5V
-3.15V is High for 74HC244, very close to 3.3V output

## Slide 11: Relay Module Construction
Notes: Talk about Ethernet Connection
-Had to make my own eagle library.

## Slide 12: Relay Module Schematic
Notes: Go over how it works

## Slide 13: Continued

## Slide 14: Ethernet Connection Interface
GND
INPUT1
INPUT2
INPUT3
INPUT4
VCC1
VCC2

## Slide 15: Raspberry Pi Development Board
Purpose/Requirements
  Protect Raspberry Pi pins
  Provide Analog to Digital inputs
  Provide PWM outputs
  Include an RJ45 Connector to control relay Module
  Allow option to power from external power source

## Slide 16: Currently Available Boards
The Gertboard – designed by Gert Van Loo: $30
Notes: Talk about stats of the gertboard
-This thing is a BEAST
-Cost more than the Pi
-Still requires use of breadboard
-Learning curve very high, harder then raspberry pi
-So popular they limit the order quantity to 1

## Slide 17
PiFace Expansion Board – Developed by the University of Manchester School of Computer Science: $20
Notes: Talk about the profits available just from these development boards.
-Piface can only program in scratch or python.
-Uses an i2c expander chip for outputs – I have already gone over the reasons

## Slide 18: My Design

## Slide 19: My Design
Analog Input/ Digital out
3.3V
3.3V
GND
GND
GND
Digital IO/ PWM
Digital Out
Digital Out
Alternate Supply (5V)
Power Source Select
I2C Access
Microcontroller
Buffer IC
GPIO Header

## Slide 20: Board
Notes: Board for anybody who is interested
-Note the artistic flair

## Slide 21: Analog to Digital and PWM
Utilizes a Microcontrollers Analog channels and PWM outputs
Communication over UART Serial
Developed custom protocol to communicate with the Raspberry Pi
  Able to configure pins as input and output
  Analog input functionality
  PWM outputs
  All commands are send using only a single byte

## Slide 22: Serial Communication
1010 1100
Program Flag
Set/Get
Flag
Analog/Digital Select
PWM
Flag
Pin 1
Pin 2
Pin 3
Pin 4
Notes: Everything uses one byte except for pwm

## Slide 23: Dev Board Python API
Layer of abstraction for ease of use
Functions Include
  setRelay(num, state)
  setOutput(num, state)
  pinMode(AorD, direction)
  digitalWrite(num, state)
  digitalRead(num)
  analogRead(num)
  analogWrite(num, value)
Live Demo

## Slide 24: Examples
Twitter Example
  Program monitors twitter for any tweet containing #SUUEET
Gmail Example
  Turns light on when a new message is present, off after its been read
SMS Example
  ????

## Slide 25: Future Work
Facebook Support
C Support
Build Enclosure
Web interface

## Slide 26: Thank You
Questions?